## Slide 1
MASTERS RESEARCH PRACTICUM · PHASE 2
Understanding Road-Crack Topology
with Graph Neural Networks
An image → graph → GNN pipeline, evaluated rigorously — with an honest look at how much the GNN actually contributes.
Tejas Shivakumar · Progress review meeting · 29 June 2026
Notes: Open with the one-liner: we built a complete image-to-graph-to-GNN pipeline that proves a GNN can understand crack topology — the prerequisite for evolution prediction. We have results, and three decisions I'd like your sign-off on.

## Slide 2
WHERE WE STARTED
The mandate — three research threads
1
Pure CV vs Hybrid
Does adding a GNN actually help crack segmentation vs a plain computer-vision model? (24 Oct)
OPEN
2
Link prediction
Transform the crack into a graph and predict how it evolves over time. (07 Nov)
REFRAMED
3
Node classification
Classify severity / type of crack portions — feasibility depends on the dataset. (07 Nov)
PLANNED
Recent professor email: follow the minutes, understand & tune the model, test on PaveDistress, and meet by mid-June.
Crack Topology GNN · Practicum Phase 2
2
Notes: Frame the whole meeting around these three threads. Thread 1 is the original core question and is still open. Thread 2 we reframed and need sign-off. Thread 3 is planned and PaveDistress unlocks it.

## Slide 3
WHAT WE BUILT
A complete three-stage pipeline
STAGE 1
Segmentation
HybridGraphUNet:
ResNet34d + ViG GNN
bottleneck + UNet decoder
RGB image → crack mask
›
STAGE 2
Image → Graph
Skeletonise → sknw graph;
6 node + 7 edge features
(deterministic, no training)
mask → PyG graph
›
STAGE 3
GNN topology proof
5 encoders (MLP/GCN/SAGE/
GINE/GAT); mask & reconstruct
hidden nodes & edges
graph → hidden structure
Status: all three stages built and working. Supporting work: data cleaning (11,298 → 4,769 images), structural clustering, and a 29 Jun evaluation-integrity fix pass.
Crack Topology GNN · Practicum Phase 2
3
Notes: Walk left to right. Emphasise that Stage 2 is deterministic preprocessing, not a model. Stage 3 is where the research claim lives.

## Slide 4
RESULT · STAGE 1 + ABLATION
Segmentation works — but the GNN doesn't help
0.722
crack IoU on DeepCrack
beats the 0.65–0.70 target ✓
but that's a different, cleaner dataset
crack_seg_clean (50ep) | Crack IoU
Plain ResNet34d — no GNN | 0.6375 ◄ best
Hybrid — ResNet34d + GNN | 0.6299
Enhanced — scratch + GNN | 0.6268
The ablation answers the original question: on crack_seg_clean the GNN bottleneck adds nothing — a plain pretrained ResNet34d matches or beats it. Pretraining is the dominant factor.
Crack Topology GNN · Practicum Phase 2
4
Notes: Two honest messages. DeepCrack 0.722 is a strong number but on a cleaner dataset. The ablation on crack_seg_clean shows the GNN bottleneck does NOT improve segmentation — plain ResNet34d (0.6375) edges out the hybrid (0.6299). This directly answers the professor's original 'does the GNN help?' question: not here.

## Slide 5
RESULT · STAGE 3 — CORRECTED
GNNs add a small gain — features do the work
Chart: 
| MLP (no graph) | GCN | GAT | GINE | SAGE
Node Average Precision (per-graph) | 0.67 | 0.6 | 0.609 | 0.687 | 0.688
+0.02
node AP — best GNN (SAGE 0.688) over the structure-aware MLP (0.670)
Correction: our earlier +47% was a size-confounded global-pooling artifact. Per-graph AP is the correct estimator — and it shrinks the gap. Heuristics (CN/AA/RA) are near-random (~0.52); structural node features carry the signal.
Crack Topology GNN · Practicum Phase 2
5
Notes: Own the correction. The +47% was inflated by global pooling letting big graphs dominate. Per-graph AP (correct) gives MLP 0.670, SAGE 0.688 — a small +0.02 gain. The honest story: structural features (degree, endpoint flags) do most of the work; message passing adds a little; classical heuristics fail entirely on these tree-like graphs. Single seed — needs error bars before claiming the +0.02 is significant.

## Slide 6
THE BRIDGE — WHY THIS MATTERS
Reconstructing hidden topology is the
prerequisite for predicting evolution
True evolution prediction needs time-series crack data — the same crack over time — which no public dataset has.
So we prove the prerequisite: new crack segments form at existing tips. We hide tips and ask which visible nodes lost a neighbour — exactly the next-growth-direction signal.
Same logic as masked-language pretraining (BERT): prove understanding via reconstruction, then transfer. We never claim to predict evolution — we prove the foundation.
Notes: Memorise this. If asked 'how does masking prove anything about evolution?', this is the 60-second answer. Lead with the honesty: no temporal data exists, so we prove the prerequisite.

## Slide 7
WHAT I NEED FROM YOU TODAY
Three decisions for sign-off
1
Thesis framing, given the small GNN gain
Keep "GNNs understand topology" (framed honestly as a small gain + heuristic-floor result) — or pivot the headline to the pipeline + methodology + CrackMark tooling?
2
Sign off the link-prediction reframe
Topology completion (mask & reconstruct) as the Phase 2 deliverable, since no temporal dataset exists. Still the right scope?
3
PaveDistress direction
Test generalisation only — or add a crack-type classification head (longitudinal / transverse / map)? Best remaining shot at a clean positive result.
Crack Topology GNN · Practicum Phase 2
7
Notes: The real purpose of the meeting. #1 is the big one now: the corrected results make the topology thesis modest, so you need the professor's steer on framing. Get explicit answers on all three.

## Slide 8
DISCLOSED PROACTIVELY
Done vs still-open — full transparency
Item | Status | Note
Baselines, heuristics, masking ablation | ✓ Done | all run — gap closed
Methodology fixes (AP, per-graph, leakage) | ✓ Done | corrected the +47% artifact
Stage 1 GNN ablation | ✓ Done | result: GNN doesn't help
Single seed — no error bars on +0.02 gap | Open · High | 3-seed runs next
50-epoch (200-ep run started, unfinished) | Open · Med | finish the run
End-to-end pipeline never run | Open · High | 10–20 images, ~2 h
No unified written report | Open · High | drafting
Crack Topology GNN · Practicum Phase 2
8
Notes: Lead with what's DONE — the rigor work closed the credibility gaps. Then the open items. The single-seed point matters more now because the GNN gap is only +0.02.

## Slide 9
PATH TO FINAL SUBMISSION
Prioritised plan
NOW
Settle the framing + test significance
Agree thesis direction with you · 3-seed runs for error bars on the +0.02 gap · end-to-end demo
NEXT
Finish the runs
Complete the 200-epoch run · PaveDistress generalisation (no GNN retraining)
THEN
The upside + write-up
Crack-type classification head (best shot at a positive result) · final research report
Crack Topology GNN · Practicum Phase 2
9
Notes: Show momentum and direction. Order is deliberate: cheapest, highest-credibility items first.

## Slide 10
IN ONE LINE
A complete, rigorously-evaluated pipeline — with honest findings and a clear decision to make about the thesis.
Segmentation solid (0.722 on DeepCrack); GNN ablation negative
GNN adds a small node-task gain (+0.02); heuristics near-random
3 decisions for your steer — framing is the big one
Thank you — questions & discussion
Notes: Close on the three decisions. Hand back to the professor for discussion.